## Slide 1: Fiber to the MDU Unit The time is now!
Your Optical Fiber Solutions Partner®
All Rights Reserved, Copyright © OFS Fitel, LLC 2022

## Slide 2: OFS – Reliable, Innovative, Global
OFS and Furukawa Global Reach

## Slide 3: Bell Labs fiber heritage
3

## Slide 4: An original inventor of fiber
40+ year history in fiber technology
Technology Emmy Award winner, 2017
  “Pioneering Invention and Deployment of Fiber Optic Cable”
Fiber manufacturing method, IEEE Milestone Recipient
  <250 granted in the history of electricity
  Others include AC power, Maxwell’s equations, telephone, television, etc.
Hundreds of patents including the LC connector

## Slide 5: Industry Stewards
OFS takes seriously its leadership role as a steward for industry change, viability, and innovation.
Our professional memberships show the breadth of this commitment:

## Slide 6: MDUs first
Faster to install
Less expensive
Typically shorter lead times
Newer technology
More viable regulatory environment

## Slide 7: Fiber Pathway Challenges
Sometime no pathways, core drilling may be needed
Pathways may be restricted in size and/or be occupied
Building owners want installation completed quickly
Fiber must be hidden or inconspicuous
Core Drilling: loud, disruptive, and expensive (up to $1000s/building)
Existing duct, already occupied
Older buildings may have no riser space

## Slide 8: Fiber Pathway Challenges
Restricted / no pathways
Corners
Fiber terminal deep inside office or living unit
Quick and hidden installation desired
Surface mounting may be the only option

## Slide 9: EZ Bend® and InvisiLight® Optical Solutions
InvisiLight MDU and Facade Solutions
Existing buildings
4 - 16 fibers in hallways
InvisiLight ILU / Office Solution
Existing buildings
1 or 2 fibers inside the unit
EZ-Bend® Solutions
New and existing buildings
1 , 2, or 4 fibers to each unit

## Slide 10: All of these use EZ Bend Fiber
Buildings have many corners
  Standard SMF will attenuate
EZ-Bend Fiber
  2.5 mm bend radius can handle any corner (and many corners) - best competitor is 5 mm
OFS Labs Patented Original Innovation – (Resonance Assisted Fiber)
Millions of homes/businesses already connected

## Slide 11: Why EZ Bend Fiber
Optical Fiber Bending Loss Increase vs Wavelength
Macro-bending Loss of typical standard G.652D SMF
Single 360 degree turn (maximum loss)
0
5
10
15
20
1260
1280
1300
1320
1340
1360
1380
1400
1420
1440
1460
1480
1500
1520
1540
1560
1580
1600
1620
Wavelength (nm)
Macrobending Loss (dB)
10 mm radius
std SMF
7.5 mm radius
std SMF
5 mm radius
std SMF
Tighter bends and longer wavelengths mean more loss with traditional fibers

## Slide 12: Why EZ Bend fiber?
G.652.D Specification
30 mm
10 mm
7.5 mm
2.5 mm
5 mm
16 mm
G.652.D from OFS
G.657.A1
G.657.A2
G.657.B3
OFS EZ-Bend fiber
Diameter of Loop Loss Specification

## Slide 13: Why EZ Bend Fiber?
Application | Standard | Current Generation |  | Next Generation on Same Fiber Network |  | Bending Loss Increase
FTTH | IEEE | GE-PON downstream | 1490 nm | 10G E-PON downstream | 1577 nm | 3X
 | ITU-T | G-PON Downstream |  | 10G-PON (XGS) downstream |  | 
 |  |  |  | 40G-PON (NG-PON2) | 1603 nm | 4X
DOCSIS and HFC | SCTE /ITU | RF-Video downstream | 1550 nm | RFoG upstream | 1610 nm | 2X
Metro and some Long Haul | ITU | C-Band DWDM /CWDM | 1560 nm | L-Band DWDM /CWDM | 1625 nm | 2.5X
Next generation systems use longer wavelengths – more bend loss

## Slide 14: Drop applications in a hallway
Hallways have many 90° angles
Hallways with recessed doors may have 4 angles per door
Recessed Doors

## Slide 15: Building anatomy and technology choices
Material Cost
Variables to consider
Riser Space
Labor cost
Aesthetics
Time in building
MDU Solutions – Mix and Match
Fiber Distribution Devices (indoors or outdoors)
Fiber Distribution Devices (with or without splitters, with or without adapters)
SlimBox (Indoor) 12,24, 64 fibers
400A (Indoor)
Up to 64 fibers
SlimBox (Outdoor)
12,24, 48 fibers
V-Linx FDH,(Indoor) Up to 144 fibers
Vertical and Horizontal Cabling Options (Outdoor)
InvisiLight Facade
EZ Bend Bundles
Intermediate connection devices
Intermediate Connection and Splicing Devices (Optional)
SlimBox (Indoor) 12,24, 64 fibers
V-Linx Terminal (Up to 24 fibers)
V-Linx Combiner (Up to 72 fibers)
SlimBox Rosette
Available pathways
In Living Unit Cabling
In Living Unit Options
EZ Bend (3.0/4.8)
InvisiLight ILU
SlimBox Wall Plate
Riser/Vertical Cabling Options
Horizontal and Drop cabling
Vertical and/or Horizontal Cabling Options (Indoor)
EZ Bend (3.0/4.8)
InvisiLight MDU
HomeRun (Drop Ceilings)
Riser cabling options
Cost
Pathways
Residents

## Slide 16: EZ-Bend® cable - Ruggedized 4.8 and 3 mm cords
Available black or white
4.8 mm black available with toning wire
  Can be direct buried
Riser (OFNR) / FT-4, Plenum (OFNP) / FT-6
  Indoor / Outdoor Rated
Available in a box or as assemblies
  Factory terminated up to 300 ft lengths
  SC Connectors for 4.8 mm and 3 mm
  SC or LC connectors for 3 mm
4.8 mm
3.0 mm
4.8 mm

## Slide 17
Your Optical Fiber Solutions Partner® Copyright © 2022 OFS Fitel, LLC. All Rights Reserved.
NOT SEEING IS BELIEVING.
MDU
ILU
Drop
Facade
Discrete and easily installable solutions for buildings and homes with the InvisiLight® MDU, ILU, Drop, and Facade Solutions

## Slide 18: InvisiLight ® MDU Solution for hallways and risers
Virtually invisible
Preferred by building owners and tenants vs. molding.
Faster and easier to install
$50 to $100 lower cost per door passed vs. molding systems.
Very visible
Disrupts Décor
Slow installation
InvisiLight
12 fiber cord
Molding
Conventional Hallway Fiber
InvisiLight MDU Solution

## Slide 19: InvisiLight® MDU 12 fiber hallway installation

## Slide 20: InvisiLight® MDU Solution – System Components
Bulk 2mm Cord,
12 fibers
Reel in Box (RIB)
2,000ft (610m)
Hole Plug and Cap
Adhesive Tool and Adhesive Tubes Ordered Separately
Point of Entry (POE) module
Factory Terminated
2mm Cord,
12 fibers
MPO, SC, or LC
or
Connector pull-through tool
(attaches to “fish stick”

## Slide 22: Installation technique – down the hallway

## Slide 23: Installation technique – unconnectorized

## Slide 24: Adding a subscriber
Slit jacket in 2 places with Jonard access tool
Add connector, groom, plug in
Mark the cord (while in the POE module)
Cut and pull back the fiber

## Slide 25: InvisiLight® Indoor Living Unit (ILU) and in-Office Solution

## Slide 26: InvisiLight® ILU – System Components
26

## Slide 27: EZ Hide – Primarily for wall-mounted ONTs

## Slide 28: SlimBox 64
Starting point for many in-building networks
Uses DirectConnect splitters
InvisiLight MDU/Façade part numbers optimized for use with SlimBox 64 FDH
  Breakout lengths
  Upjacketing

## Slide 29: Examples

## Slide 32: InvisiLight® Whole Building Installation - 4 floors 60 units
Service Provider will later plug EZ-Bend ® jumper to optical modem from this point
Point of entry module - from hallway to each unit or office

## Slide 33: Case Study – 48 unit building

## Slide 34: Initial installation – InvisiLight MDU
4 floor building – 48 customers
Wired from FDH to ONT in approximately 3-4 days
  InvisiLight ILU in units
  InvisiLight MDU in risers and hallways
Building owner pleased
Optically tested fine

## Slide 35: Survey math
180’
Telecom and electrical closet
Hallway
6’
40’ up riser (for longest length)
360’ down hallway (2x)
48’ 4’ slack in 12 point of entry modules
12’ ends of hallway
15’ in closet
15’ extra
490’ (150m) Total
155m lengths ordered…no length issues
12’
FDH

## Slide 36: Tools used – complete list in installation documents
Skewers for fiber access
Removable clips, glasses, headlamp, scissors

## Slide 37: Beginning of process
Place point of entry modules
Completely unspool from FDH location
Plug in later
With firestop and InvisiLight ILU added
Cord coming out from riser in telecom closet

## Slide 38: Additional prep work if needed
Inside and outside bend limiters at corners
Through wall tool and wall plugs/caps
3/8” (10mm)
Hole drilled outside of telecom closet. Tape eventually removed

## Slide 39: Use clips to hang cord above each doorway
Clip applied, slack is good
Repositionable clips

## Slide 40: Cord pulling and takeup
Take up on empty spool using broomstick and box
Cord is very light weight
Cord should have very little tension even over long distances
Stop pull and look for obstacles if significant tension is felt
Concern is more for fiber crushing than excess tension

## Slide 41: Wheels can be very helpful
Wheeled scaffolding is very effective
  Speeds up adhesive and cord placement processes
  Smooths out adhesive installation process
Painter’s tape before and after POE and around corners can be helpful to speed installation

## Slide 42: Adhesive process – pictures not from the trial
Apply very thin adhesive bead…thinner is better!!
Apply long stretch to allow it to turn tacky (<10-15 minutes, typical)
Press cord into adhesive with finger
Keep a wet rag handy to remove excess!

## Slide 43: Adhesive process
Thinner bead is better
Expect 65-100’ (20-30 m) per tube
OFS testing shows approximately 100’ (30m)/tube
Installers typically use less as experience grows

## Slide 44: Adhesive and loops
Finished module with 3 wraps of cord
Keep cordage slack enough to pull back and make 3 wraps inside module
Adding adhesive and loops

## Slide 45: Connecting a customer
Make a mark on all wraps at the bottom of the module
Remove cord from module
Slit here
Slit here

## Slide 46: Slit cord at marked locations
Slit cord with Jonard tool at two outside marks (1/2-1” (12-25 mm) working inward
Cut fiber at slit farthest from FDH
Pull back fiber from other slit

## Slide 47: Add connector, mark ID, groom, close

## Slide 48: Fusion splice-on connector process
4 loops used inside Point of Entry module
  Enabled enough length to splice on top of ladder
After connector added, groom cord
Add fiber and connector last

## Slide 49: The finished hallway – where’s the fiber?

## Slide 50: Additional pictures

## Slide 52: Additional pictures from properties

## Slide 55: InvisiLight Facade
What is it?
  Cord and installation system for vertical or horizontal outdoor deployments
    12 fibers - 3.0 mm
    24 fibers – 3.8 mm
  Ultra bend-insensitive optical fiber for very tight indoor bends
    Meets Telcordia GR-326 and GR-1435 standards
  Materials compliant with flammability/smoke regulations
    UL Riser/FT-4 rating

## Slide 56: System components – InvisiLight Facade
Fasten with “Shark’s Tooth” cable clip model BT187SK100 or similar. (Not purchased from OFS).
Bare or Preconnectorized Indoor/Outdoor Multifiber Cord – 12F, 24F
Point of entry modules with connector adapter

## Slide 57: Sample pictures, InvisiLight Facade

## Slide 59: Different configuration
4 fiber SlimBox
InvisiLight Façade Cord
EZ Bend to each unit
In unit to ONT
Field installable connector
Wall plate (optional)

## Slide 60: InvisiLight® Façade Solution
InvisiLight® Façade Installation
InvisiLight®
24 Fiber Cord
Rejected by MDU Property
Accepted by MDU Property
$10 - $20 saving per apartment vs. molding+cords
InvisiLight® Façade Bulk Cord,
Fibers 3mm OD
24 Fibers 3.8 mm OD
Reel in Box (RIB)
Cords in Molding
Slimbox® Enclosure on Façade or in attic

## Slide 61: InvisiLight® Façade/Breezeway Applications
UV Resistant Compact POE
12 and 24 Fiber Façade Cables
with EZ-Bend® Fiber

## Slide 62: 4 buildings, 8 units/each, 4 units upstairs, 4 units downstairs

## Slide 63: Fiber layout
8 units per building, 12 fiber cord
Complicated layout
45 90 degree angles, splitter to ONT
0.5 dB total loss from splitter to ONT including 2 splices and 2 connection points
Customer was very pleased
Second floor
First floor
Vertical path
Horizontal path

## Slide 64: Downstairs

## Slide 65
Stairwells

## Slide 66: Upstairs

## Slide 67: Unit 103 – InvisiLight ILU
600 micron InvisiLight was completely invisible
Some problems unspooling fiber
InvisiLight is almost completely invisible on that surface

## Slide 68: General recommendations – outdoor MDU pathways
EZ Bend (3.0/4.8)
Smaller buildings and garden style apartments
Mid-size and larger buildings
Spliced or pre-connectorized available
InvisiLight Facade
EZ Bend Bundles
Typically pre-connectorized on subscriber end

## Slide 69: General recommendations – indoor MDU pathways
EZ Bend (3.0/4.8)
When to use intermediate connection devices
Smaller buildings and garden style apartments
Mid-size and larger buildings
InvisiLight MDU
HomeRun (Drop Ceilings)
SlimBox (Indoor) 12,24, 64 fibers
V-Linx Terminal (Up to 24 fibers)
V-Linx Combiner (Up to 72 fibers)
When riser space is limited
Reduce cords/cables in a riser (8-10 is typical max)
For wall surface mount applications
For drop ceiling applications
Spliced or pre-connectorized available

## Slide 70: FTTx and In Building Solutions for the Entire Passive Network
http://www.ofsoptics.com/fttx-solution-offering.html